## Slide 1: MODFLOW 6 Overview

## Slide 2: background

## Slide 3: History
1970’s proliferation of groundwater models led to numerous diverging codes within the USGS
The best capabilities were combined to form MODFLOW

## Slide 4: MODFLOW 1984 and 1988

## Slide 5: MODFLOW Development and use in the USGS
Office of
Groundwater
Water Science
Centers
National Research
Program

## Slide 6: MODFLOW Core Versions
1984
1988
1996
2000
2005
What do we mean by “core” version?
Production version
Stable
Well documented
Well tested
Long-term funding
Starting point for new developments
Notes: Production codes
Well tested
USGS headquarters supported

## Slide 7: Philosophy of a “Production Code”
Easy to understand
  Finite difference
  Well documented
Extensible
  Modular design
Portable
  use standard FORTRAN
Efficient (memory and speed)
  Judicious incorporation of new capabilities
  Exclude functionality that can be done outside

## Slide 8: MODFLOW Philosophy
Maintain production version
Keep MODFLOW lean!
  Anything that can be done outside of MODFLOW should be done outside MODFLOW (e.g., no dates and times)
You can’t accommodate everyone
Encourage others to enhance MODFLOW
Release new capabilities in different versions
No dependencies
Periodically update production version with proven advancements

## Slide 9: MODFLOW-2000 Example
New processes added to MODFLOW
  Observations (OBS)
  Sensitivity (SEN)
  Parameter Estimation (PES)
Resulted in thousands of lines of new code
  Code become very complicated
Generalized parameter estimation programs became the norm (e.g. PEST)

## Slide 10: MODFLOW-2005
Code redesigned to improve memory handling
Removed SEN and PES

## Slide 11: USGS MODFLOW Versions (since 2005)
2005
2015
2010

## Slide 12: Common Themes
Coupled models and packages
  Pipe flow (CFP, USG)
  Surface water flow (SFR, LAK, SWR)
  Unsaturated flow (VSF, UZF)
  Solute transport (GWT)
  Variable-density flow and transport (SEAWAT)
  Watershed (GSFLOW)
  Agricultural demand (OWHM)
Unstructured/asymmetric solvers (NWT, USG, SWR, CFP)
Multiple models and packages
  Local grid refinement (MF-LGR)
  Multiple packages of the same type (CDSS)

## Slide 13: MODFLOW 6

## Slide 14: MODFLOW 6 Development
Consolidate popular capabilities from MODFLOW versions (2005, NWT, USG, LGR, …)
Improve solution technique
Modernize code and input structure
Support multi-model simulations
Extend MODFLOW into a hydrologic simulator
New core version
1984
1988
1996
2000
2005
2017
Notes:     MODFLOW 6 will combine the best features of existing versions of MODFLOW and get rid of outdated functionality. Highly coupled and complex systems will be solved with one system of equations making this MODFLOW version much faster than with previous versions of MODFLOW that iteratively solved the flow part, then the other parts, like transport or local grid refinement. This effort intends to modernize MODFLOW’s design to account for 20+ years of improvements in software design and essentially making MODFLOW a more of a hydrologic simulator.

## Slide 15: MODFLOW 6
Object oriented
  Multiple models
  Multiple packages
Control volume finite difference formulation
Regular grids or unstructured grids
Traditional or Newton Raphson formulation
New look and feel
Available now (6.0.4)

## Slide 16: MODFLOW 6 Publications
Hughes, J.D., Langevin, C.D., and Banta, E.R., 2017, Documentation for the MODFLOW 6 framework: U.S. Geological Survey Techniques and Methods, book 6, chap. A57, 40 p., https://doi.org/10.3133/tm6A57.
Langevin, C.D., Hughes, J.D., Banta, E.R., Niswonger, R.G., Panday, Sorab, and Provost, A.M., 2017, Documentation for the MODFLOW 6 Groundwater Flow Model: U.S. Geological Survey Techniques and Methods, book 6, chap. A55, 197 p., https://doi.org/10.3133/tm6A55.
Provost, A.M., Langevin, C.D., and Hughes, J.D., 2017, Documentation for the "XT3D" option in the Node Property Flow (NPF) Package of MODFLOW 6: U.S. Geological Survey Techniques and Methods, book 6, chap. A56, 40 p., https://doi.org/10.3133/tm6A56.

## Slide 17: USGS Support Software
MF5TO6
  Included with MODFLOW 6
ZONEBUDGET
  Included with MODFLOW 6
FLOPY for MODFLOW 6
  Available now
MODPATH 7
  Available for certain types of grids
MODELVIEWER
  Beta available
MODELMUSE (Winston)
  Beta version available
Notes: Chris

## Slide 18: MODFLOW 6 FRAMEWORK

## Slide 19: Simulation Components
Timing Module
Solutions
Models
Exchanges
Utilities
Simulation
Solution 1
Model 4
Timing Module
Model 1
Model 3
Model 2
Exchange 1
Exchange 2
Exchange 3

## Slide 20: Timing Module
TDIS Package
  Uses the MODFLOW concepts of stress periods, time steps
Alternative timing packages may be developed in the future
Timing applies to all models

## Slide 21: Solutions
Used to solve one or more models and exchanges
The only solution available now is the Iterative Model Solution, or IMS
  Unstructured and asymmetric
IMS solves the following nonlinear equation
  Ax = b

## Slide 22: Multi-Model Simulation
MODFLOW 6 foundation allows models to be tightly coupled at the matrix level
Allows local grid refinement (LGR), and other model coupling strategies

## Slide 23: LGR Simulation
Simulation
Iterative Model Solution
PARENT
Temporal Discretization
C1
GC
C2

## Slide 24: GWF Exchanges
Simulation
Iterative Model Solution
PARENT
Temporal Discretization
C1
GC
C2
PARENT-C1
PARENT-C2
C1-GC

## Slide 25: LGR Simulation
Simulation
Iterative Model Solution
PARENT
Temporal Discretization
C1
GC
C2
PARENT-C1
PARENT-C2
C1-GC
BEGIN OPTIONS
END OPTIONS
BEGIN TIMING
TDIS6 mysim.tdis
END TIMING
BEGIN MODELS
GWF6 parent.nam PARENT
GWF6 c1.nam C1
GWF6 c2.nam C2
GWF6 gc.nam GC
END MODELS
BEGIN EXCHANGES
GWF6-GWF6 parent-c1.exg PARENT C1
GWF6-GWF6 parent-c2.exg PARENT C2
GWF6-GWF6 c1-gc.exg C1 GC
END EXCHANGES
BEGIN SOLUTIONGROUP 1
IMS6 mysolver.ims PARENT C1 C2 GC
END SOLUTIONGROUP
Simulation Name File

## Slide 26: Matrix-Level Coupling
Simulation
Iterative Model Solution
PARENT
Temporal Discretization
C1
GC
C2
PARENT-C1
PARENT-C2
C1-GC
Notes: Because our solver is unstructured and asymmetric, can handle Newton-Raphson, unstructured grids, ghost nodes, XT3D, dispersion tensors, etc…

## Slide 27: Groundwater flow (gwf) model

## Slide 28: GWF Model Highlights
Generalized control-volume finite-difference formulation
  Regular MODFLOW grids
  Unstructured grids
IDOMAIN capability
Full 3D anisotropy
Multiple stress package ”instances”
Water Mover
New input structure

## Slide 29: Finite-Difference Equation

## Slide 30: Generalized CVFD Equation

## Slide 31: Rearranged for Solution

## Slide 32: CVFD Accuracy Considerations
Line connecting cell centers bisects shared face at a right angle
Line connecting cell centers does not bisect shared face at a right angle

## Slide 33: Spatial Discretization
Three ways to enter grid
  DIS – regular MODFLOW grid
  DISV – discretization by vertices
  DISU – fully unstructured

## Slide 34: Discretization (DIS) Package
“Regular MODFLOW grid”
Consists of layers, rows, and columns
Top and bottoms can have variable elevations

## Slide 35: Discretization by Vertices (DISV)
Boundary fitted grids!
Allows unstructured grids to be constructed using common mesh generators
Layered

## Slide 36: DISV (cont.)
User provides
  List of x,y vertices
  List of vertices for each cell
MODFLOW determines cell connectivity

## Slide 37: DISV (cont.)
Cells are referenced by (layer, cell number)
Not immune to CVFD accuracy considerations

## Slide 38: Ghost-Node Correction (GNC) Package
standard finite volume formulation
head at ghost node
optional formulation in MODFLOW
ghost-node formulation
Notes: Developed by Edwards, Mehl and Hill, etc.
Limitation of standard finite volume formulation: line connecting two nodes must intersect shared edge at a right angle.
Alpha parameters can be calculated to include effects of heterogeneity

## Slide 39: Ghost-Node Example

## Slide 40: Simulation Errors

## Slide 41: IDOMAIN Capability
Improve efficiency for models with large areas of inactive cells
Address MODFLOW limitations with discontinuous hydrogeologic layers

## Slide 42: IDOMAIN Capability (cont.)
Permanently remove a cell from the simulation
Can be used with DIS and DISV
Optionally connect overlying and underlying cells

## Slide 43: Representation of Anisotropy
Representation of full 3D anisotropy may be required for some problems (fractured aquifers, structurally deformed aquifers)
Some capabilities available (LVDA, SUTRA), but needed generalized CVFD method

## Slide 44: Groundwater Flow Equation
Traditional MODFLOW
Generalized 3D Anisotropic Flow

## Slide 45: Hydraulic Conductivity Ellipsoid
Defined by three user-provided values on a cell by cell basis
For unrotated case,
  K11 = Kx
  K22 = Ky
  K33 = Kz
K11
K22
K33

## Slide 46: Ellipsoid Rotation
Users can optionally provide ANGLE1, ANGLE2, and ANGLE3 on a cell by cell basis
ANGLE1 is counter-clockwise rotation in the x, y plane

## Slide 47: Ellipsoid Rotation (cont.)
All three angles can be specified to represent ellipsoid orientation

## Slide 48: Effective Conductivity Approach
Large errors for certain ellipsoid configurations
Approximate, but relatively fast
Simple to implement

## Slide 49: XT3D Approach
General and robust handling of anisotropy
Computationally expensive
Improves flow solution for certain grid types
Is being used for dispersion

## Slide 50: All GWF Packages

## Slide 51: Multiple Package of Same Type

## Slide 52: Water Mover (MVR) Package
Need trackable way to transfer available water from one package to another
  Previously hardwired (e.g., LAK <> SFR, DRT)
MODFLOW 6 has generic capability to move water from a “provider” to a “receiver”
Provider packages:
  WEL, DRN, RIV, GHB
  MAW, SFR, LAK, UZF
Receiver packages:
  MAW, SFR, LAK, UZF
Notes: WEL: available water is pumping rate
DRN: QA is groundwater flow into the drain
RIV: QA is groundwater flow into the river
GHB: QA is groundwater flow into the GHB
MAW: QA is the actual rate of pumped water
SFR: QA is the outflow for the specified reach
LAK: QA is the outflow at a lake outlet
UZF: QA is the rejected infiltration

## Slide 53: Under development

## Slide 54: Current Efforts
Subsidence Package
XT3D across models
MPI parallelization
Generalized particle tracking
Groundwater Transport GWT Model
  Unstructured grids
  XT3D for dispersion
  Transport through cells that are “dry”
Variable Density Groundwater Flow and Transport
  Unstructured grids
  Support for Newton (hydraulic head formulation)
Linear Network Flow (LNF) Model
Landscape Hydrology Model

## Slide 55: Henry-Like Wetting/Drying Problem
Seawater Tidal Boundary
Freswhwater Inflow Boundary
Notes: Velocity-based dispersion coefficients

## Slide 56: MODFLOW 6 Animation
Notes: 10 seconds to run this.